## Slide 1: Car2X Communication
Florian Janßen, Hagen schmidtchen,
paul bergmann, johannes Windelen

## Slide 2: Project Goal
Allow cars to communicate with each other and with control stations
Exchange diagnostics
Receive situational information and emergency broadcasts
Information gain leads to improved path planning and car control

## Slide 3: Pre-midterm
Reading the documentation and getting into the previous group‘s code
Installation and tutorials for the Altera Quartus software (FPGA)
Learn about the Nios II and multicore implementations on FPGA
Planning the Car2X Protocol and the general hardware setup
Current WIP:
Basic Quartus hardware implementation
Experiments with the wireless converter hardware
Setting up PC as car2x station

## Slide 4: Post-midterm
  Hardware (THE BIG ONE)
      Ethernet controller
      Memory problems
      Timing problems
      .... problems
  We also implemented a lot of software
      Telnet server
      Message handler
      Shared Memory controller
      Testing GUI

## Slide 5: Hardware Setup (on car)
H-Bridge
4x

## Slide 6: Hardware Setup (FPGA)
JTAG UART
Shared
Memory
Ethernet
System
CarControl
Nios Core
OnChip
Memory
Communication Nios Core
SDRAM

## Slide 7: Hardware Setup (FPGA - QSYS)

## Slide 8: Hardware Setup (FPGA - Hierarchy)
QSYS
entity
Net
PLL
RAM
PLL
Net
DDIO
IO Pin
Planer
Toplevel file

## Slide 9: Hardware Setup (Problems)
Partially bad tutorials (copy paste  “It works”)
Combine different tutorials
No/very few Verilog/VHDL skills
Broken Board
Never sure, where the error comes from (HW, SW, Eclipse, …)!

## Slide 10: Hardware Setup (Problems)

## Slide 11: WiPort configuration
Configuration:
  Access point
  Client mode
  Static IP
WiPort
Ethernet
Client
IP
Client
IP
Client
IP
Server
Client

## Slide 12: Communication Flow
Image processing
Motor controllers
WiPort
Switch
Altera FPGA
Other sensing
Telnet CarProtocol
+ C2XExtensions

## Slide 13: Communication Core
Runs MicroC OS: Multithreading
3 Threads:
  Socket Server (OUR TASK)
  Inet Main (OS)
  Clock Tick (OS)
TCP server implemented with Nichestack TCP / IP suite
Can accept multiple connections (WiPort, wheels, camera, ...)

## Slide 14: Communication Core Workflow
Wheels
WiPort
Camera
Client
Connections
TCP Server
Telnet
Connection
Buffers
C A R P ...
Parser
Execute Commands
Shared Memory
Packet
Data

## Slide 15: Memory controller
  Supports multiple shared memory areas
  One hardware mutex per area
  Instantiate a MemController for each Area
  API:
    get(idx), getLast(), getAll(), clear(), push()
Comms Core
MemController
Control Core MemController
Mutex 1
Shared memory |  | 
Area 1<CarState> | Area 2<int> | Area 3<float>
CarState content[] | int content[] | float content[]
index | index | index
maxElements | maxElements | maxElements
Mutex 2
Mutex 3

## Slide 16: Car Control Core
  State machine based on Operating mode: idle, autonomous, remote control, emergency brake
    Sets car parameters (max speed)
  Calculates the velocities of the individual motors
  Modular idea: run image processing, more fancy control code.

## Slide 17: C2X protocol: the packets
‘C’ | ‘A’ | ‘R’ | ‘P’
packet counter |  | payload length | 
type | … | length | …
payload |  |  | 
type | … | length | …
payload |  |  | 
C2X protocol header
Car Message 1
Car Message 2

## Slide 18: C2X protocol: what‘s supported
Available message types:
  0x30 - State
  0x60 - RemoteControl
  0x08 - GoalPose
  0x01 - EmergencyBrake
  0x02 - MotorVelocity
  0x03 - MotorMeasurement
‘C’ | ‘A’ | ‘R’ | ‘P’
packet counter |  | payload length | 
type | … | length | …

## Slide 19: C2X protocol: what‘s supported
Available message types:
  0x30 - State
  0x60 - RemoteControl
  0x08 - GoalPose
  0x01 - EmergencyBrake
  0x02 - MotorVelocity
  0x03 - MotorMeasurement
‘C’ | ‘A’ | ‘R’ | ‘P’
0x0000 |  | 0x0008 | 
0x60 | … | 0x04 | …
0x10 | 0x15 | 0x10 | 0x15

## Slide 20: GUI

## Slide 21: Further Steps (HAGEN)
Documentation
Get the system running ... Usw